## Slide 1: Energy systems in Israel, Palestine and Jordan
Aman Majid, Nurit Gal, Suleiman Halasah, Michael Gilmont, Jim Hall
Understanding the potential for regional cooperation
Oxford Martin School, University of Oxford
June 2022

## Slide 2: Background

## Slide 3: Background
Historical emissions

## Slide 4: Background
Climate commitments
NDCs: GHG reductions | Israel | Jordan | Palestine
2030 | 27% | 31% | -
2040 | - | - | 26.6% or 17.5%
2050 | 100% | - | -
Israel to phase-out coal by 2026
Israel to increase renewable shares to 25% and 30% in 2025 and 2030
Palestine plans to convert Gaza diesel plant to gas
No specific renewables targets for Palestine
Renewable targets | Israel | Jordan | Palestine
Today | 8.5% | 20% | 5%
2030 | 30% | 50% | 20%

## Slide 5: Speed and scale
Could level of ambition to decarbonise be increased?
The global power sector is not aligned with the Paris agreement
Numerous institutions (e.g., IPCC, IEA, CAT) calling for rapid and massive scale-up of renewables to 2030
Investing in fossil assets risks carbon lock-ins and stranded assets
Could cooperative energy policy could unlock deep decarbonisation in the region?
JORDAN
ISRAEL

## Slide 6: The regional energy landscape

## Slide 7
West Bank: 1.16 MWh/person
Gaza:

## Slide 8: Solar and wind potential

## Slide 9: Trends
Costs of renewable energy technologies declining
Carbon reduction commitments (NDCs)
Varying potential of wind and solar across the region
Power demand patterns vary seasonally due to differences in cooling/heating demands and in energy-intensity
Increasing demand for desalination and air conditioning
Palestine still lacks reliable electricity supplies
Consideration of transboundary energy transfers (Prosperity Green project)
Energy demands

## Slide 10: Issues
Israel:
  Struggling to increase renewable capacity
  Land allocation permits for renewable difficult to obtain
Jordan:
  Demand does not match solar generation curves
  Could have excess curtailment
  Grid stability issues
Palestine:
  Power supplies still unreliable
  Gaza electricity access is poor
  Wants to increase self-sufficiency

## Slide 11: Our project

## Slide 12
Plan energy systems to 2030 while considering:
  Decarbonisation goals
  Renewable goals
  Regional cooperation

## Slide 13: Methods

## Slide 14: Model Inputs
Growth projections
Hourly demand
Wind generation
Solar generation
Operational rules
Technical constraints
Scenarios
Level of Cooperation
Self-sufficiency targets
Emissions
targets
Renewable targets
Applies only to Palestine
Model
CAPACITY EXPANSION MODEL
SIMULATION MODEL
Optimisation algorithm chooses a mix of technologies that meets targets at lowest cost
Computer model simulates how system would perform under new technology mix
Results
Capacities
Dispatch curves
Renewable curtailment
Costs
Technology mix
Emissions

## Slide 15
https://github.com/amanmajid/nextra

## Slide 16: Scenarios
Increasing cooperation
NCO
COO
BAU
BAS
Increasing
decarbonisation ambition
All scenarios meet:
Future demands
Renewable targets
Palestinian self-sufficiency

## Slide 17: Limitations
Estimated data for Jordan and Palestine
  Electricity demand curves
  Generation curves
  True RES capacity factors
Transmission constraints
System features (e.g., efficiencies and losses; operational rules etc.)
Modelled outputs presented here will be different from bottom-up estimates within countries

## Slide 18: Preliminary Results

## Slide 19: Costs
BASELINE
BUSINESS-AS-USUAL
COOPERATION
NON-COOPERATION
9.4%
Reduction in costs relative to current plan (BAU)
x2.4
Investment in Jordan increases relative to current plan (BAU)

## Slide 20: Capacities
24%
Reduction in build-out of solar and battery storage compared to current plan (BAU)
x2.2
Total capacity needed in Jordan compared to current plan

## Slide 21: Electricity flows
NCO
COO
x20
More renewable curtailment in non-cooperative (NCO) operations compared with cooperative (COO) case

## Slide 22: Renewable uptake
Utilisation under non-cooperative and cooperative operations
>90%
Daily renewable utilisation under COO
Jun-Aug
Generally exhibit greatest levels of renewable uptake. Excess supplies during Feb-Apr.

## Slide 23: Self-sufficiency
Capacity changes due to Palestine’s self-sufficiency targets
8%
Reduction in Israel’s total capacity requirements between 10-100%
x12
Total capacity increase in Palestine between 10-100% self-sufficiency
Based on current operational configurations (BAU)
Notes: Can we disaggregate this by technology (e.g. Fossil and Renewable)?

## Slide 24: Deep decarbonisation
XX%
Reduction in costs relative to current plan (BAU)
22%
Less capacity of renewables and storage needed under cooperative (COO) system
$47 billion
Total saving to achieve net zero by 2030 under cooperative (COO) energy policy
How could cooperation deliver net-zero?
Total capacities of solar, wind and storage
Values aggregated for Israel, Jordan and Palestine

## Slide 25: Conclusions

## Slide 26: Results
Summarising our findings
Cooperative (COO) energy planning and management has significant benefits:
  Reduce costs by 28% compared to current plan (BAU)
  Improves renewable energy uptake and reduces curtailment
Pursuit of self-sufficiency (NCO) is challenging:
  Much higher renewable build-out with greater curtailments
  Costs almost twice as much as the cooperative case (COO)
  Very large costs for Palestine
Scale and ambition could be increased:
  To align regional power sector with Paris agreement
  Working to net zero cooperatively (COO) is much more economical

## Slide 27: Supporting slides

## Slide 28: Scenarios
Baseline (BAS):
  No consideration of sustainable development goals;
  Continue with business-as-usual practices;
  Quantifies minimum infrastructure needed without sustainable transitions
Business-as-usual (BAU):
  Continue with current practices;
  Develop sustainably: observing renewable/carbon targets;
  Palestine aims for minimum level of self-sufficiency (30%)
Non-cooperation (NCO):
  Develop sustainably: observing renewable/carbon targets;
  Zero cooperation between regions;
  Each region acts as an energy island
Cooperation (COO):
  Develop sustainably: observing renewable/carbon targets;
  Complete cooperation between regions (i.e., unlimited energy trading);
  Palestine aims for minimum level of self-sufficiency (30%)
Increasing cooperation
NCO
COO
BAU
BAS
Increasing
decarbonisation ambition

## Slide 29: Capacities

## Slide 30: Next steps
Sense-check our scenarios and results
Scope feasible options for cooperative energy management
Further opportunities to explore: e.g., the role of green hydrogen

## Slide 31: Battery usage
State-of-charge (SOC) under NCO and COO
Need to further analyse:
The daily SOC under COO is generally lower; particularly around summer months. This helps RES uptake to increase — why does this not happen under NCO?

## Slide 32: Renewable cost curves